## Slide 1
OXYGEN PLANT-
Tonnage Cryogenic Plant
What is Oxygen Plant /O2N2 Plant /ASU ?
Why it is needed. Oxygen or Nitrogen ?
Every 1 % of O2 Enrichment increase productivity by 2.5-4 %

## Slide 2
Air Separation Process Overview
Main Air Compressor
DCAC & EVC
Pre- Purification Unit

## Slide 3
Liquid O2
Liquid N2
Molecular
Sieves
Turbine
DCAC
Air
Waste N2
High Pressure
Column
Low Pressure
Column
Gaseous N2
Gaseous O2
Main Heat
Exchanger
Subcoolers
Air separation
MAC
EVC
HEATER
N2
O2
CT

## Slide 4
Liquid O2
Liquid N2
Molecular
Sieves
Turbine
DCAC
Air
Waste N2
High Pressure
Column
Low Pressure
Column
Gaseous N2
Gaseous O2
Main Heat
Exchanger
Subcoolers
Single line diagram
MAC
EVC
HEATER
N2
O2
Air separation process
PSA type - Pressure swing adsorption.
- Less than 25 TPD plant & less purity 93%.
VPSA type - Vacuum s\pressure swing adsorption..
- 25 to 75 TPD & less purity 93%.
Cryogenic type :
75 to 5500 TPD
high purity 99.95% & multi products.
CT

## Slide 5
Compression & Purification
Air filtration-0.4 micron-92%
Air compression
4.5 bar g at 40 C
Air cooling
up to 16 C.
Air purification-Co2/H20- Nil.

## Slide 6
Cold Box –Equipment's
Cold box:
Main heat Exchanger
Distillation columns-LP/HP
Exp. Turbine.
Outer box with perlite powder.

## Slide 7
Product Supply-SVD
Compressor:
N2 compressor-02 nos , screw type.
O2 compressor
01 no- Reciprocating .
SVD:
Lox tank
30 T @ 0.2 bar
Lin tank
30 T @ 4 bar
Liquid product
Liquid purchase

## Slide 8
Application of O2
O2 Application
HBS Cold blast - O2 Enrichment-
Cast - lancing
PCM -scull cutting
Sinter m/c-
O2 Enrichments
Blast Furnace area
Sinter Plant
6” pipeline
2.5” pipeline
O2N2
5” flow control valve
6” ON/OFF
Ball Valve
8
Application of N2
N2 Application
GCP- puffing, purging
Furnace- BLT cooling, ,lance flushing
PCM- De-dusting puffing.
PCI- grinding mill & tank pressuring
BFG line purging.
ONLINE Analyzer purging
Blast Furnace area
Sinter Plant
6” pipeline
4” pipeline
O2N2
6” flow control valve
LOX
LIN
PIC-Auto valve

## Slide 9
Oxygen Plant-2 (VPSA type)
Type :VPSA Oxygen Plant.
Oxygen flow -:3500Nm3/hr,93%,
BF3-: 2500Nm3/hr,
BF1/2-: 500 Nm3/hr

## Slide 12
Oxygen Plant- (VPSA type)

## Slide 13
Nitrogen PSA Plant

## Slide 14
Nitrogen PSA Plant
Type of Plant: PSA Nitrogen Generator
Nitrogen flow: 800Nm3/hr ,
Purity : 98% ,
Pressure : 7 barg ,
Adsorbent: ZMS (Zeolite molecular sieve)